## Slide 1: A Packet-Interleaving Scheme for Reliability Resilience under Burst Errors in Wireless Sensor Networks
Author: Tsang-Ling Sheu and Yen-Hsi Kuo
Publisher: ICN 2016
Presenter: Yi-Hao Lai
Date: 2016/08/31
Department of Computer Science and Information Engineering
National Cheng Kung University, Taiwan R.O.C.
Notes: 1
blocked TCAMs: SmartPC
power reduction on average (88%).
wastes considerable TCAM capacity

## Slide 2: Introduction
To effectively deliver the collected data back to a control center for further analysis, a wireless sensor network (WSN) is usually built.
However, packet transmission over a WSN may encounter intermittent errors due to weak signals or interferences. The erroneous packets, if comprising of text or numbers, such as temperature or humidity, would require packet re-transmission, which increases network load.

## Slide 3: Introduction
Thus, the motivation of this paper is to increase transmission reliability over a WSN.
Researches on transmission reliability over a WSN can be divided into two major categories
  reliable routing
  information coding
Notes: 2 bitmap types

## Slide 4: Reliable routing
To increase the transmission reliability after data are collected by a sensor node, relay nodes (RNs) are employed.
R. Sampangi, utilized RNs to divide sensors into several cluster networks. Since the distance from a sensor to its cluster head is reduced, the quality of data transmission is greatly improved.

## Slide 5: Information coding
E. Byrne, designed a coding scheme which can increase the probability of successful decoding based on graph theory.
Y. Hamada, proposed a scheme to reduce packet error rate by using Luby Transform (LT) codes. Their proposed scheme has achieved small complexity of O(n).

## Slide 6: Propose scheme
We propose a packet interleaving scheme (PIS) based on Reed-Solomon (RS) codes to reduce the impact of burst errors on packet uncorrectable probability.

## Slide 7: Multi-hop Tree Structure
In a wireless sensor network (WSN), a coordinator is the sink which gathers all the data collected from other distant sensor nodes.

## Slide 8: Packet Interleaving
In the proposed PIS, packets collected by a sensor node are classified into two different types: high-reliability required (HRR) packet and non-HRR packet.
It is better to employ a shorter-length symbol (in this paper, we use m = 4) to encode an HRR packet with shorter data length.
Longer-length symbol (we use m = 8) to encode a non-HRR packet with longer data length.

## Slide 9: RS symbol
An HRR packet is encoded with a shorter-length RS symbol (i.e., m = 4).

## Slide 10: Packet Interleaving
When both an HRR and a non-HRR packet are received by a branch node in a tree-structured WSN, these two packets are interleaved on a symbol-by-symbol basis.
Notes: R3 R8

## Slide 11: Packet Interleaving
However, an interleaved packet may not be correctable, if it encounters burst errors where the number of total errors is greater than t.

## Slide 12: UBEM (uniform bit error model)
= 1 -
= 1 -
= 1 -

## Slide 13: OBEM on-off bit error model

## Slide 14: Performance

## Slide 15: Performance

## Slide 16: Performance