## Slide 1: Source Routing with Protocol-oblivious Forwarding to Enable Efficient e-Health Data Transfer
Author: Shengru Li, Daoyun Hu, Wenjian Fang and Zuqing Zhu
Publisher: 2016 IEEE International Conference on Communications Presenter: Yi-Tsung Huang
Date: 2017/02/22
Department of Computer Science and Information Engineering
National Cheng Kung University, Taiwan R.O.C.
Notes: 1

## Slide 2: Introduction
In order to support Big Data applications more efficiently, WANs also need a more programmable and adaptive architecture with effective network control and management (NC&M), which is similar to the innovation trends in other types of networks.
Thanks to the advances on SDN, the Big Data related traffic can be managed more efficiently in WANs.

## Slide 3: Introduction
However, due to the large-scale and geographically-distributed nature of WANs, the scalability could become a critical issue when incorporating SDN for WANs.
Specifically, when the traffic volume increases, more and more flow-tables will be installed in the switches, which can use up their memory, make the table look-up and traffic scheduling increasingly complex, and increase the communication overhead significantly.
Notes: This is because OpenFlow defines protocol-dependent flow-matching rules, which can lead to repeated flow-table installations and look-ups in the forwarding plane.

## Slide 4: Introduction
In this paper, we design and implement a novel network system that can leverage source routing with POF to facilitate efficient e-Health data transfers with low setup latency.
We develop the POF-based source routing protocol, and experimentally demonstrate that with the proposed scheme, the flow-tables installed in each core switches in a POF-controlled SD-WAN can be minimized.

## Slide 5: POF Primer
Basically, POF inherits the network architecture of OpenFlow.
However, the innovations provided by POF are the protocol-oblivious description for 􀃀flow-matching fields and a set of generic flow instructions, with which protocol-independent packet forwarding can be realized easily in the switches.

## Slide 6: POF Primer

## Slide 7: POF Primer
Matching Fields: POF simply defines the search key of a matching field as a tuple <offset, length>.
POF-FIS: All the instructions in POF-FIS utilize the tuple <offset, length> to locate the data that they need to operate on.

## Slide 8: POF Primer
Flow Tables: The flow tables stored in a POF-enabled switch can be classified into four types, i.e., the masked-match(MM), the longest-prefix-match(LPM), the exact-match(EM) and the direct table(DT).
Metadata Memory: When a switch needs to handle multiple tables in packet forwarding, it uses metadata memory to store the flow information that the current table processing generated for the next.

## Slide 9: POF-based Source Routing in SD-WAN

## Slide 10: POF-based Source Routing in SD-WAN - Packet Design for Source Routing
The packet fields can be tailored specially to enable efficient source routing.

## Slide 11: POF-based Source Routing in SD-WAN
The ingress edge switch stores the output ports in its metadata memory, and will insert them into every packet of the flow by using POF-FIS.
The subsequent core switches use a pre-installed pipeline-like matching rule that consists of multiple flow tables to process the packets.

## Slide 12: POF-based Source Routing in SD-WAN

## Slide 13: POF-based Source Routing in SD-WAN

## Slide 14: Experimental Demonstration

## Slide 15: Experimental Demonstration

## Slide 16: Experimental Demonstration
Notes: 用mininet模擬，一直增加core switch